## Slide 1: One Water: The Power of One and the Promise of Many
CWEA WEBINAR, August 24, 2022

## Slide 2: Brian Peck
MODERATOR Project Manager
Project Partners
Notes: Please DON’T put speakers agency logo on the slide. It will not look good.

## Slide 3: UPCOMING EVENTS
Oct
18th
Seismic Considerations For Water Infrastructure: Displacement Hazard
Analysis And Soil Liquefaction
SARBS Online Webinar Series
TBD
Achieving Class A Biosolids With Temperature Phased Anaerobic Digester Facility
SARBS Online Webinar Series

## Slide 4: This is made possible by the following sponsors

## Slide 5
Zoom Controls: Chat for Comments

## Slide 6
Zoom Controls: Q&A for Questions

## Slide 7
Zoom Controls: Raise Hand Feature Not Used in Today’s Webinar

## Slide 8
Watch for The Attention Check Code in Top LEFT Corner of Screen
Attention Check Code
####

## Slide 9
Process for Claiming Contact Hours for
this Webinar
Note the different attention check code(s) that will appear for 60-90 seconds in the top left or right corner of the presentation.
Log in to https://owen.cwea.org/ the Online Wastewater Education Network (OWEN) with your mycwea.org account info and find this program in “Your Dashboard”.
Under the "Contents" tab, enter the correct attention check codes in the “Attention Check Code” component within 48 hours of the live webinar.
Your contact hours will be reflected in your mycwea.org account within 2-3 weeks following completion.

## Slide 10
Slides/Handouts Can Be Found on OWEN under the Handouts Tab

## Slide 11
CWEA, its Board members and
volunteers are not responsible for the
actions of speakers or the content of their
sessions. No endorsement is implied or
given of any persons or their philosophies,
ideas or statements; nor of any products
or processes; nor of any organizations
or companies who volunteer to serve as
speakers in educational programs.
For reporters: all speakers today are off the record.

## Slide 12
Integrated Solutions Director Black & Veatch
Zeynep Erdal

## Slide 13: SARBS Professional Development Committee
Zeynep Erdal, PhD, PE
Integrated Solutions Director
One Water: The Power of One and the Promise of Many August 24, 2022
Santa Clara Valley Water District – Advanced Water Purification Center

## Slide 14: Agenda
What Is Water Resilience - Defining the Problem
One Water Improving Water Resilience
Case Studies
Q&A

## Slide 15: What is Water Resilience?
Having a reliable water supply that can adapt and respond to change
Reliability/Adaptability
  Affordable
  Treatment flexibility to manage variable feed water quality
  Robust to produce high quality treated water
  Minimize environmental pollution
OCWD/OCSD – Groundwater Replenishment System

## Slide 16
State of Water Industry
$$ is the main concern
Treatment technologies – “we got this!”
Additional challenges on the way
Bridging “today” to a resilient future – how to best do it?

## Slide 17
Increasing Demand on Water Resources

## Slide 18
Water Resources are Inextricably Tied to Other Resources – Energy, Nutrients and Food

## Slide 19: Groundwater Extractions and Subsidence
Source: USGS.gov
Limited withdrawals
Subsidence
Seawater intrusion

## Slide 20: Climate Change Resulting in Water Quality Changes
Algal blooms
Point- and non-point sources of pollution
Fires and hurricanes

## Slide 21: Wastewater Discharge Limitations
Increasingly restrictive water quality requirements for municipal effluent
Elimination of WW discharges and ocean outfalls through regulatory action
Eastern Treatment Plant – Melbourne, AU
Hampton Roads and Norfolk, VA

## Slide 22: Managing Future Water Challenges
Water challenges are inevitable
Growing water stress
Climate change amplifying and extending pressure on our systems
These challenges drive utilities to evaluate water reuse to provide a resilient water supply – even in locations previously considered water rich.
Source: A. Boretti and L. Rosa, “Reassessing the projections of the World Water Development Report” NPJ Clean Water (2019)
Notes: )

## Slide 23: One Water Improving System Resilience

## Slide 24: Our Water Cycle Is Connected, Driving Supply Reliability and Resilience

## Slide 25
Circular Economy for Resource Circularity
“an industrial system that’s restorative or regenerative by intention
and design. It replaces the end-of-life concept with restoration,
shifts towards the use of renewable energy, eliminates the use of
toxic chemicals that impair reuse and return to the biosphere, and
aims for the elimination of waste through the superior design of
materials, products, systems and business models.”

## Slide 26
Resource Cycle for Larger Impact
Facility Costs
Optimum Point for the System?
Resources Recovered
Carbon Footprint
Balancing Impacts and Costs

## Slide 27: Water Reuse – All Types – Integral to One Water
Reuse increases water supply without requiring new water sources.

## Slide 28: Example Potable Reuse Treatment Trains
Source: 2017 Potable Reuse Compendium (USEPA 2017)
Reverse Osmosis
TDS, inorganic, and organics removal
Ozone + BAF/GAC
Organics removal
Ozone + BAF/GAC + RO
Improved operation
Capital and operating cost savings
Multiple barriers

## Slide 29: Full Advanced Treatment Is the Benchmark
Carbon Based Alternative Technology Can Reduce Implementation Costs

## Slide 30: Case Studies

## Slide 31
Paso Robles, CA
Phased Implementation - Phase 0: Recycled Water and Sustainability Plans - Phase I: Facility upgrades, reuse system, sustainable solutions – renewable energy, bioswales, permeable pavements, natural hot springs for heating, nutrient recovery and fertilizer production - Phase II: NPR pipe network
Sustainable by Design
Reuse | Non-potable
Partners | Agricultural Local Commercial
Location | CA
Climate | Coastal
Recovered Resources | Water Nutrients Energy

## Slide 32
Coachella Valley Water District, CA
Making low tech work for sustainable design
Reliable water supply for agriculture and local community
Reuse | Non-potable
Partners | Agricultural Local Community
Location | CA
Climate | Arid/Desert
Recovered Resources | Water (Nutrients, Energy)

## Slide 33
City of Escondido, CA
Phased Implementation - Phase 0: One Water Plan and Implementation Roadmap - Phase I: MF/RO facility for high-quality recycled water to irrigate 1,500 acres of avocado crops - Phase II: AWT for highly purified water for IPR/DPR
Reuse | Non-potable, Potable
Partners | Agricultural Local Community
Location | CA
Climate | Coastal
Recovered Resources | Water Energy

## Slide 34
Large Scale Impact Through Whole System Solutions -- Singapore
Reuse | Non-potable Potable
Partners | Agricultural Industrial Commercial Public
Location | Singapore
Climate | Tropical
Recovered Resources | Water Nutrients Energy Space/Land

## Slide 35
Large Scale Impact Through Regional Solutions – Examples from Southern California
City of San Diego, CA, Pure Water Program
City of LA, CA, Operation NEXT Program
LACSD/MWD, CA, Regional Recycled Water Program
87 mgd
150 mgd
180+ mgd

## Slide 36: Orange County Water District Ground Water Replenishment System
World’s largest system for IPR
Protect groundwater basins from seawater intrusion
Replenish local groundwater supplies
Provides new potable water for ~850,000 residents

## Slide 37: Reuse can provide water resilience
Drought
Groundwater
Water Quality Change
Cost
Discharge Limitations
Upon looking at holistic costs – utilities are finding reuse to be a financially attractive means to solve multiple issues.
OCWD/OCSD – Groundwater Replenishment System
OCSD Clarifiers

## Slide 38: NEWater Singapore

## Slide 39: Singapore’s One Water: “National Taps”
  Land size ~300 square miles
  Population ~ 5.5 million
Public Utilities Board (PUB)
  Provides management and regulation of water supply
Singapore Supplies
  Collected Rainfall
  Imported Water from Malaysia
  Reclaimed Water (NEWater)
  Desalinated Water
  Future sources
Singapore is a highly dense region that implements diverse water supply portfolio with reuse being a primary supply.

## Slide 40: NEWater Factories of Singapore
NEWater plants currently supply up to 40% of Singapore's current water needs; by 2060 this is expected to increase to 55%
Facility | CAPACITY (mgd) | Product Water Uses
1Changi | 60 | Indirect potable reuse Wafer fabrication Other non potable and industrial applications
2Bedok | 22 | 
1Ulu Pandan | 38 | 
2 Kranji | 38 | 
1 Plants owned and operated by a concession company under DBOO arrangement
2 Plant owned and operated by PUB
Notes: About 160 mgd of total capacity.

## Slide 41: Deep Tunnel Sewerage System – Investment That Pays off
The DTSS was developed to meet Singapore’s long term clean water needs through collection, treatment, reclamation and disposal of industrial and municipal used water
Massive network of deep tunnels to convey domestic water to centralized WRPs
Designed to provide “100 years of maintenance- free design life”
Phase 1 DTSS
  Provides used water to Changi WRP
Phase II DTSS
  Extends tunnels west to Tuas WRP and NEWater Factory

## Slide 42: Resource and Water Resilience
Ulu Pandan Wastewater Treatment Plant – Singapore
Changi NEWater Plant – Singapore
Tuas Integrated Facilities – Singapore

## Slide 43
Advanced Water Purification Center (AWPC) Santa Clara Valley Water District, CA
Attention Check Code:
9172

## Slide 44: Silicon Valley Advanced Water Purification Center (AWPC)
This project has won several awards including Water Reuse National Project of the Year and Global Water Intelligence Association Reuse Plant of the Year
Partnership Santa Clara Valley Water District (SCVWD) and the City of San Jose, CA
Source water secondary effluent from the San Jose-Santa Clara Regional Wastewater Facility
Goal: produce high purity recycled water to reduce existing recycled water salinity and increase marketability of existing recycled water supply
Attention Check Code:
9172

## Slide 45: Silicon Valley Advanced Water Purification Center (AWPC)
PURIFICATION PROCESS | FUNCTION | NET CAPACITY (MGD) | SPECIAL REQUIREMENTS
Microfiltration/ Ultrafiltration | Pretreatment of nitrified secondary effluent to reduce TSS | 10.5 | Preselection of MF/UF mfg’s
Reverse Osmosis | TDS reduction | 8 | Decarbonization process to stabilize product water
Ultraviolet Disinfection | Disinfection of product water | 10 | NWRI Guidelines UV Validation Preselection of mfg’s
Silicon Valley AWPC uses a multiple-barrier approach for advanced potable-ready reuse
Attention Check Code:
9172

## Slide 46: Resilience
Water quality and public perception were major drivers.
Diversify water sources
Secure drought-proof supply
Reduce discharge into San Francisco Bay
Improve public acceptance of recycled water
SJ/SC Water Pollution Control and Purification Facilities
Attention Check Code:
9172

## Slide 47: Eastern Treatment Plant Melbourne Australia
Attention Check Code:
9172

## Slide 48: Non-RO based Reuse – Melbourne
$10M pilot program with 16 processes
$440M x 220 MGD Reuse Facility
World’s Largest Reuse Facility
Upgraded in 2012 to provide Class A Water
REUSE FACILTY FLOW DIAGRAM
8-years of full-scale data
Attention Check Code:
9172

## Slide 49: 220 mgd Advanced Tertiary Treatment Plant
Class A Water
Fit-for-use
International Awards
Drought
Groundwater
Water Quality Change
Increasing Cost of Status Quo Approaches
Discharge Limitations
Attention Check Code:
9172

## Slide 50
Conclusions and Recommendations
Whole system considerations result in larger scale impact – water, energy, food security essential
Need to replace the “single value” mindset with “multiple value” essential resources in planning
Instead of “taking the waste out” need to “supply, recover and restore resources”
Partnerships with industries to optimize water, resource and financial resilience
Interconnected infrastructure needs interconnected engineering and regional collaborations

## Slide 51
© 2022California Water Environment Association (CWEA)

## Slide 52: QUESTIONS & ANSWERS
Notes: Please DON’T put speakers agency logo on the slide. It will not look good.

## Slide 53
Process for Claiming Contact Hours for
this Webinar
Log in to https://owen.cwea.org/ the Online Wastewater Education Network (OWEN) with your mycwea.org account info and find this program in “Your Dashboard”.
Enter the attention codes (XXXX) in the “Attention Check Code” component under the "Contents" tab within 48 hours of the live webinar.
Your contact hours will be reflected in your mycwea.org account within 2-3 weeks following completion.

## Slide 54: This is made possible by the following sponsors

## Slide 55
© 2022California Water Environment Association (CWEA)