## Slide 1: Supercritical Water Oxidation Converting waste into water, energy and nutrients
January 17, 2023, 12:00 pm – 1:00 pm
pioneering a new era in sustainability

## Slide 2: Stephanie Douglass
Mott MacDonald
CWEA Students and Young Professionals Chair
Notes: Please DON’T put speakers agency logo on the slide. It will not look good.

## Slide 3
CWEA, its Board members and
volunteers are not responsible for the
actions of speakers or the content of their
sessions. No endorsement is implied or
given of any persons or their philosophies,
ideas or statements; nor of any products
or processes; nor of any organizations
or companies who volunteer to serve as
speakers in educational programs.
For reporters: all speakers today are off the record.

## Slide 4: Sudhakar Viswanathan
Process for Claiming Contact Hours for
this Webinar
Note the different attention check code(s) that will appear for 60-90 seconds in the top left or right corner of the presentation.
Log in to https://owen.cwea.org/ the Online Wastewater Education Network (OWEN) with your mycwea.org account info and find this program in “Your Dashboard”.
Under the "Contents" tab, enter the correct attention check codes in the “Attention Check Code” component within 48 hours of the live webinar.
Your contact hours will be reflected in your mycwea.org account within 2-3 weeks following completion.
VP of Sales
374Water

## Slide 5: Who are we?
Social impact, cleantech, vision/mission driven company in Durham, NC
2015
2013
2018
Today ($SCWO)

## Slide 6: Water 101
ice
water
vapor
100oC/212oF
94.4oC/ 202oF
Temperature
vs. Pressure

## Slide 7: What is Supercritical Water?
Water
  Universal solvent
  Readily dissociates salts (inorganic)
  Oil (organics) don’t mix
Supercritical water
  Gas like behaviour
  Liquid like density
  Salts come off solution
  Readily dissociates organics
Source: Public Domain, enviro.wiki

## Slide 8: SCWO for Organic Waste
AirSCWOTM converts organic waste into clean water, heat, electricity and CO2 in seconds!

## Slide 9: PFAS specific wastes
PFAS + O2 (air) H2O + CO2 + F- + CaF2 + heat
AirSCWOTM eliminates PFAS from spent GAC, spent IEX, RO reject, diluted AFFF, landfill leachate, groundwater, wastewater sludges & biosolids, rinsates from decontamination

## Slide 10: AirSCWOTM

## Slide 11: Sludge Chemical Transformation
99.9% COD conversion to CO2 + energy
>95% TN converted to N2
>85% PO4 precipitated as phosphorus pentoxide
Parameter | Influent | Effluent
COD (mg/L) | 220,000 | 200
VSS | 18 | 0%
Total N (mg-N/L) | 15,000 | 500
NH3 (mg-N/L) | 600 | 100
NO2- (mg-N/L) | 50 | 5
NO3- (mg-N/L) | 300 | 10
PO43- (mg-P/L) | 6000 | 150
pH | 8 | 7
Conductivity (μS/cm) | 5000 | 300

## Slide 12: Sludge Mineral Content
 | Percent (%) | Pounds per Ton | Nutrients (lbs/ton)
Nitrogen - Total | 0.14 | 2.8 | 0.84
P2O5 - Total | 19.3 | 386 | 231.6
K2O - Total | 0.4 | 8 | 6.4
Calcium | 8.9 | 178 | 106.8
Magnesium | 2.31 | 46.2 | 27.72
Sulfur | 1.3 | 26 | 15.6
Boron | 0.01 | 0.2 | 0.12
Zinc | 0.17 | 3.4 | 2.04
Manganese | 1.34 | 26.8 | 16.08
Iron | 16.68 | 333.6 | 200.16
Copper | 0.07 | 1.4 | 0.84
Sodium | 1.57 | 31.4 | 31.4

## Slide 13: Fate of Other Pollutants
Organic
Urea, ammonium
Heterocycles
Organic
Phosphate
Vent gas
N species are mostly transformed to N2 gas
Solid minerals
Phosphate precipitates Ca3(PO4)2
MgNH4PO4·6H2O
Typ. Gas composition
<3 ppmv NH3
<5 ppmv NOx
<3 ppmv SOx
No odor
HS-, COS, organic
Mercaptans
Sulfates, Hydrates
CaSO4
Emerging contaminants
Pharmaceuticals
PFAS, 1,4-D
Mineralized to CO2
Fluoride dissolved, CaF2
Metals
Dissolved
Precipitates
Non-leachable forms

## Slide 14: Fate of PFAS in solids/liquids
>99.9% PFAS destruction
99.99% elimination of PFOS
99.95% elimination of PFOA
Pollutant | In | Out*
PFBA | 5,000 - 8,000 | 99.86%
PFHxA | 3,000 - 7,000 | 99.89%
PFNA | 500 - 1,500 | 99.90%
PFDA | 3,000 - 5,000 | 99.97%
PFUnA | 500 - 1,500 | >99.89%
PFBS | 500 - 1,500 | >99.98%
PFPes | 3,000 - 5,000 | >99.98%
PFHxS | 3,000 - 5,000 | 99.99%
PFOS | 150,000 - 230,000 | 99.99%
PFOA | 2000 – 4000 | 99.95%
* Includes water, air and minerals

## Slide 15: Fate of PFAS in gasses
    EPA PITT emission tests, deployed 2 methods:
  Passivated, evacuated canisters
  Sorbent tubes
    Mass flux of volatiles organic compounds as percent of input total organic fluorine: <0.2%
    Only traces were detected in vent gas

## Slide 16: What else can SCWO treat?
Wastes Treated to Date
AFFF
AFFF Rinsate
Animal Waste
Food Waste
GAC
Ion Exchange Resin
Landfill Leachate
Microplastics
Pharmaceuticals
Straw Water
Sludges & Biosolids

## Slide 17: Other Micropollutants
Spiked contaminants in IPA/water and in biosolids
Ibuprofen and acetaminophen:
  Feedstock: 10 mg/L each
  Effluent: ND at < 1 µg/L
  DRE: >99.99%
Triclosan:
  Feedstock: 100 µg/L
  Effluent: ND at < 0.1 µg/L
  DRE: >99.9%
Triclosan
Ibuprofen
Acetaminophen

## Slide 18: AirSCWO™ Commercial Offerings
1 wtpd*
~264 GPD
@ 15%
1 tpd
26 kW
624 kW-h/day
Losses 20 kW
30 wtpd
(~8000 GPD @ 15%)
Ideal for 5 MGD WW facility
200 wtpd
(~53,000 GPD @ 15%)
Ideal for 30 MGD WW facility
167 kW
4000 kW-h/day **
12.5 kW
300 kW-h/day**
6 wtpd
(~1600 GPD @ 15%)
Ideal for 1 MGD WW facility
10 kW
300 kW-h/day
*Pilot unit – not optimized for energy efficiency
** Net electric energy after parasitic use
Heat: 80 MWh/day
Heat: 12 MWh/day
Heat: 2.4 MWh/day

## Slide 19: AirSCWO™ Commercial Offerings
 | AirSCWO™ 6 | AirSCWO™ 30
Capacity for liquid or slurry Dry solids capacity | 6 wet tons/day or 1600 gal/day ~0.5-1.5 tons/day | 30 wet tons/day or 8000 gal/day ~2.5-7.5 tons/day
Footprint | One 40 ft container | Three 40 ft container
Operation | up to ~8000 hours/year | 
Typical organic or calorific content of feedstock | ~160 g COD/L 2.5 MJ/L | 
Power usage/produced | Uses ~240 kWh/day | Produces ~300 kWh/day
Availability | Late 2022 | Late 2023

## Slide 20: AirSCWO™ Installations
Demonstration Scale (1 WTPD)
Duke University, Durham, NC:
  2013 to 2022
  < 200 runs
Kokomo, IN:
  2022 to current
  Semi-permanent install for pilot studies
Full Scale (6 WTPD)
CA - 2Q 2023
FL - 2Q 2023
ME - 2Q 2023
DoD 1 - 3Q 2023
NC - 4Q 2023
DoD 2 - 4Q 2023
4+ units to be deployed elsewhere

## Slide 21: Prefabricated, Compact & Modular
AirSCWO™ 1 metric ton per day operating on the Duke campus from 2015
AirSCWO™ 6 metric ton per day assembled at MB facility 2022

## Slide 22: Key Benefits

## Slide 23: Summary
Omniprocessor – waste agnostic
Compact modular containized system for easy deployment
Energy efficient and self sufficient
Ideal technology to meet Sustainable Development Goals

## Slide 24
pioneering a new era in sustainability
Sudhakar (Sunny) Viswanathan VP of Sales
+1 919-800-9221
sv@374water.com
374water.com

## Slide 25: THANK YOU
© 2023 California Water Environment Association (CWEA)